## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – SIH26126
Problem Statement Title – Vision Based Autonomous Navigation for Unmanned Ground Vehicle for Outdoor environment
Theme – Smart Automation
PS Category – Software
Team ID – 14
Team Name – QSLAM

## Slide 2: QSLAM — maps and vision replace GPS, end to end
QSLAM
Proposed solution
Operator gives one destination in UTM — nothing else
Stereo vision, IMU and wheel odometry carry the UGV there
Preloaded satellite / DEM maps replace the satellite fix
No GNSS receiver at any stage — nothing to jam or spoof
How it addresses the problem
Start pose and heading from map matching, no compass needed
Map re-anchoring every ~200 m keeps drift bounded on one-way runs
Semantic + 2.5D elevation perception finds safe ground
Hybrid-A* and MPPI drive it; Collision Monitor guards it
Innovation and uniqueness
★ Map-anchored global localization
Passive BEV ↔ satellite / DEM matching fixes pose, heading and drift — the role GPS used to play.
★ Localizability-aware navigation
A custom Nav2 cost layer scores feature density, so the route stays where vision keeps working.
★ Localization integrity monitor
Cross-checks VIO against IMU and wheels every cycle — degraded mode instead of silent drift.
− 88 %
position error after 3 km, no GNSS
89.6 m → 10.6 m (PoC)
− 59 %
arrival error vs traversability-only
planner, for +18 % path (PoC)
0
GNSS receivers, at any stage
of any mission

## Slide 3: TECHNICAL APPROACH
QSLAM
Technologies to be used
● Sensing
ZED X stereo camera (RGB · depth · IMU) · wheel encoders · no GNSS receiver
● Localization
Isaac ROS cuVSLAM · robot_localization EKF · cross-view BEV-to-satellite matcher · GeographicLib
● Perception
SegFormer fine-tuned on RELLIS-3D + RUGD · TensorRT · elevation_mapping_cupy (GPU)
● Planning & control
ROS 2 Nav2 · Smac Hybrid-A* · MPPI · Collision Monitor · custom C++ costmap plugins
● Platform
ROS 2 Jazzy · CUDA · C++17 / Python · Jetson AGX Orin target · Isaac Sim 6 on RTX 4090
● Maps & data
ISRO Bhuvan / Cartosat imagery + DEM, preloaded offline · RELLIS-3D, RUGD for training
Proven components reused · QSLAM adds the new modules
Methodology and process for implementation
★ marks QSLAM's own contribution
Everything else is production-grade, open-source software we reuse rather than rebuild.

## Slide 4: FEASIBILITY AND VIABILITY
QSLAM
Analysis of the feasibility — measured, not asserted
− 59 %
PoC-1 · localizability layer
arrival error vs traversability-only planner (+18 % path)
1 km synthetic terrain · 300 Monte-Carlo runs
− 88 %
PoC-2 · map anchoring
position error after 3 km with no GNSS (89.6 m → 10.6 m)
match σ 5 m · 75 % success · 300 runs
189 m
Integration testbed · Isaac Sim 6
GPS-free traverse to a UTM goal, 1.09 m drift
7 recoveries handled autonomously
Potential challenges and risks → strategies for overcoming them
Challenge / risk | Strategy for overcoming it
Start pose and heading unknown | BEV-to-satellite / DEM match gives UTM pose and heading; surveyed launch point as fallback
VIO drift on one-way runs | Re-anchor to the map every ~200 m; wheel-odometry EKF and localizability-aware routing bound the error
Goal lies beyond sensor range | Rolling global costmap; unknown cells carry an optimistic cost; Hybrid-A* replans as the map fills
Ditches, slopes and drops | GPU 2.5D elevation map turns slope, step height and roughness into costs, fused with semantic classes
Vision degrades — night, dust, low texture | IMU and wheel dead-reckoning bridge outages; degraded mode slows, then safe-stops; thermal as an upgrade
Onboard compute budget | cuVSLAM, TensorRT and CuPy keep every heavy stage on GPU; per-node latency tracked for Jetson AGX Orin

## Slide 5: IMPACT AND BENEFITS
QSLAM
Potential impact on the target audience
● Armed forces
Navigate where GNSS is unavailable, jammed or spoofed
● BEL & defence industry
Drop-in ROS 2 navigation module for existing UGV platforms
● Civil GNSS-denied users
Disaster response, mines, tunnels and dense forest
Mission applications
Reconnaissance
Border surveillance
Last-mile resupply
Hazardous / CBRN zones
Benefits of the solution
Strategic — Immune to jamming and spoofing by design — no satellite signal is used at any stage
Social / safety — The UGV takes the risky last mile; fewer soldiers exposed in hazardous zones
Economic — COTS camera and open-source ROS 2 stack; retrofits with no ground infrastructure
Self-reliance — Indigenous, auditable navigation software BEL can own, adapt and certify
Environmental — Passive sensing, no RF emissions; suits electric UGVs and cuts manned sorties
Validation targets · Isaac Sim first, then field trials
≥ 90 %
GPS-denied mission
success (A → B)
≤ 2 %
position error on
arrival, as % of distance
≤ 5 m / 2°
start alignment from
map matching
≤ 100 ms
sensing-to-command
latency
≥ 15 FPS
perception rate on
Jetson AGX Orin

## Slide 6: RESEARCH AND REFERENCES
QSLAM
Details / links of the reference and research work
Localization & SLAM
[1] Korovko et al., “cuVSLAM: CUDA Accelerated Visual Odometry and Mapping,” arXiv:2506.04359, 2025
[2] NVIDIA Isaac ROS Visual SLAM — github.com/NVIDIA-ISAAC-ROS/isaac_ros_visual_slam
[3] Cadena et al., “Past, Present and Future of SLAM,” IEEE T-RO, 2016
[4] Moore & Stouch, “Generalized EKF for ROS” (robot_localization), IAS-13, 2014
Data & tools
[14] ISRO / NRSC Bhuvan geoportal — imagery and DEM — bhuvan.nrsc.gov.in
[15] NVIDIA Isaac Sim · Stereolabs ZED X SDK · ROS 2 Jazzy documentation
Navigation & planning
[5] Macenski et al., “The Marathon 2: A Navigation System,” IROS 2020 — docs.nav2.org
[6] Macenski et al., “Cost-Aware Kinematically Feasible Planning” (Smac), arXiv:2401.13078, 2024
[7] Williams et al., “Information Theoretic MPC” (MPPI), ICRA 2017
Perception & traversability
[8] Miki et al., “Elevation Mapping using GPU,” IROS 2022 — elevation_mapping_cupy
[9] Xie et al., “SegFormer,” NeurIPS 2021
[10] Jiang et al., RELLIS-3D, ICRA 2021; Wigness et al., RUGD, IROS 2019
Basis for QSLAM innovations
[11] Costante et al., “Perception-aware Path Planning,” arXiv:1605.04151 → localizability layer
[12] Shi & Li, “Highly Accurate Vehicle Localization Using Satellite Image,” CVPR 2022 → map anchoring
[13] Sarlin et al., “OrienterNet,” CVPR 2023
★ Why these three matter
They are the published basis for QSLAM's own modules: map anchoring, the localizability layer and the integrity monitor.
Reused, proven
cuVSLAM · Nav2 (Smac, MPPI, Collision Monitor) · SegFormer · GPU elevation mapping
QSLAM contribution
Map-anchored localization · localizability layer · integrity monitor · degraded-mode policy
Next research step
Cross-view matcher fine-tuned on Indian terrain (Bhuvan / Cartosat) · thermal for night